## Slide 1
The perception of surface material from disparity and focus cues
Martin S. Banks1, Abdullah Bulbul1, Rachel Albert1, Joohwan Kim1, Rahul Narain2, James F. O’Brien2, & Gregory J. Ward3
1 Vision Science Graduate Program, UC Berkeley
2 Department of Computer Science, UC Berkeley
3 Lawrence Berkeley National Laboratory & Dolby Labs
Notes: Distinguishing materials based on their visual properties is invaluable. Distinguishing good from spoiled meat or fish. Determining the quality of the finish of an automobile or fabric. Or determining whether a surface is safe to walk on (is it solid or mushy?).

## Slide 2
Retinal image determined by:
  properties of surrounding environment
  surface geometry
  viewer’s position
  surface reflectance properties
Determining surface material greatly under-constrained
Inferring Material Properties
Notes: The problem is that the visual appearance of a surface is determined by many factors including the properties of the illuminant, the geometry of the surface, the viewer’s position, and of course the reflecting properties of the material itself. Because of this identical materials can create quite different retinal images. Similarly, very different materials can create rather similar images.

## Slide 3
Image statistics
  highlights are bright & desaturated
  skew of luminance histogram (Motoyoshi et al., 2007)
  curvature flow (Fleming, 2014)
Inferring Material Properties
Notes: Change 2, get the same image

## Slide 4
Image statistics
  highlights are bright & desaturated
  skew of luminance histogram (Motoyoshi et al., 2007)
  curvature flow (Fleming, 2014)
Natural viewing
  binocular
  motion
  accommodation & blur
Inferring Material Properties
Notes: Great majority of studies in vision science literature use pictures of objects composed of different materials. People are reasonably good at categorizing materials despite impoverished viewing condition. Here we consider the additional information provided by binocular viewing when either the object or viewer might be moving. And importantly, how accommodation (focusing the eye to different distances) coupled with blur can help distinguish material properties.

## Slide 5
specular
Lambertian
Reflections from Different Materials
complex

## Slide 6
specular
Lambertian
Reflections from Different Materials
complex
Bidirectional Reflectance Distribution Function (BRDF)

## Slide 7
Binocular Disparity
z0
z1
I
XL
XR
where
in radians
left eye
right eye
Held, Cooper, O’Brien, & Banks (2010)
s0

## Slide 8
b1
in radians
Focus & Blur
A
s0
z0
z1
Held, Cooper, O’Brien, & Banks (2010)

## Slide 9
Triangulation Cues to Depth
z0
z1
baseline
XL
XR
binocular disparity
motion parallax
blur

## Slide 10
Reflection Geometry: Disparity
left & right eyes
illumination sphere
object
virtual image
left & right eyes
Kirschmann (1895)
Blake & Bülthoff (1990)
Muryy, Fleming, & Welchman (2013)

## Slide 11
illumination sphere
object
virtual image
Reflection Geometry: Disparity
left & right eyes
Kirschmann (1895)
Blake & Bülthoff (1990)
Muryy, Fleming, & Welchman (2013)

## Slide 12
Reflection:
virtual image with uncrossed disparity
Paint: same highlight with zero disparity
Reflections & Disparity

## Slide 13
object
virtual image
pupil aperture
illumination sphere
Reflection Geometry: Blur

## Slide 14
illumination sphere
object
virtual image
Reflection Geometry: Blur
pupil aperture

## Slide 15
focus on surface
Reflections & Blur
focus on reflection

## Slide 16
focus on surface
Reflections & Blur
focus on reflection

## Slide 17
      Multi-plane Display
Do vergence-accommodation conflicts in stereo displays cause discomfort & fatigue?
If so, what can we do to minimize the discomfort & fatigue?
Love, Hoffman, Hands, Gao, Kirby, & Banks (2009)

## Slide 18
Switchable Lens
Birefringent material (e.g., calcite) has ordinary & extra-ordinary refractive indices depending on polarization
Calcite lens has two focal lengths Fo & Fe
Variation in power effected by polarization modulator (FLC)
Can stack lenses; 2N states
Love, Hoffman, Hands, Gao, Kirby, & Banks (2009)

## Slide 19
lens in near state
lens in near-mid state
lens in mid-far state
lens in far state
      Changing Focal Distance
Love, Hoffman, Hands, Gao, Kirby, & Banks (2009)

## Slide 20
      Multi-plane Display
Love, Hoffman, Hands, Gao, Kirby, & Banks (2009)

## Slide 21
siʹ
p1
p2
p3
p4
si
=
ki1 ∗
ki2 ∗
ki3 ∗
ki4 ∗
+
+
+
Optimized Blending

## Slide 22
siʹ
p1
p2
p3
p4
si
=
ki1 ∗
ki2 ∗
ki3 ∗
ki4 ∗
+
+
+
Optimized Blending

## Slide 23
Stereo
Motion
Blur
Stimulus Conditions

## Slide 24
Experimental Stimulus: Stereo
reflection
Notes: Is this pinhole rendering?

## Slide 25
Experimental Stimulus: Stereo
paint
Notes: Is this pinhole rendering?

## Slide 26
Experimental Stimulus: Stereo
reflection
Notes: Is this pinhole rendering?

## Slide 27
Experimental Stimulus: Stereo
paint
Notes: Is this pinhole rendering?

## Slide 28
Stereo
Motion
Blur
Stimulus Conditions

## Slide 29
Experimental Stimulus: Motion Parallax
reflection
Notes: Is this pinhole rendering?

## Slide 30
Experimental Stimulus: Motion Parallax
paint
Notes: Is this pinhole rendering?

## Slide 31
Stereo
Motion
Blur
Stimulus Conditions

## Slide 32
Experimental Stimulus: Volumetric
camera focused on surface

## Slide 33
Experimental Stimulus: Volumetric
camera focused on reflection

## Slide 34
Experimental Stimulus: Volumetric
camera focused on surface

## Slide 35
Experimental Stimulus: Volumetric
camera focused on reflection

## Slide 36
Experimental Procedure
Stimuli
textured flattened ovoids; four different textures
material rendered according to Ward’s isotropic BRDF model
  specular reflection or slightly rough specular
  Lambertian analog to both
distant environment map for illumination
duration = 4 sec
Response measure
subjects indicate perceived glossiness of each stimulus on 0-9 scale
15-min training session with no feedback to anchor scale
Subjects
four young adults with corrected-to-normal acuity (three naïve)
264 observations per subject (12 presentations of 22 conditions)

## Slide 37
Results: Disparity
Notes: No cues yielded slightly higher gloss rating than stereo on surface

## Slide 38
Results: Disparity
Sakano & Ando (2010)
Wendt, Faul, Ekroll, & Mausfeld (2010)
Notes: No cues yielded slightly higher gloss rating than stereo on surface

## Slide 39
Results: Motion Parallax

## Slide 40
Results: Motion Parallax
Sakano & Ando (2010)
Doerschner et al. (2011)

## Slide 41
Results: Blur
Notes: No cue had slightly higher gloss rating than single-plane with blur, but lower than volumetric.

## Slide 42
Average Results: Roughness = 0
**
**
**
**
**
**
**
p < 0.01
Wilcoxon signed-rank test
Disparity
Motion parallax
Blur

## Slide 43
Average Results: Roughness = 0.01
**
n.s.
**
n.s.
**
n.s.
n.s. not significant
**
p < 0.01
Wilcoxon signed-rank test
Disparity
Motion parallax
Blur

## Slide 44
Conclusions
Reflections from specular surfaces with smooth geometry create virtual reflection images distinguishable from the surface by disparity, motion parallax, & blur.
Humans use each of those reflection cues—in isolation and in combination—to estimate surface gloss. The novel observation is that blur is used.
When surface material is rough, virtual reflection images become less distinct.
Pinhole rendering of reflections, which is commonplace, is inappropriate because humans use focus cues to estimate gloss.
Funding from NSF & NIH

## Slide 45
z0
z1
M
XL
XR
in radians
time 1
time 2
Motion Parallax
s0

## Slide 46
Hartung & Kersten (2002)
Motion Parallax

## Slide 47: Previous work on triangulation cues and material perception
Perception of gloss is enhanced by
  Changes in illumination with observer motion
  Differences between the two eyes in the luminance of an area
No previous work on blur and material perception
Sakano & Ando (JOV, 2010)

## Slide 48: Example layers (optimized blending)
Original scene
mid-near
far
near
far-mid
Layers
Courtesy of Rahul Narain

## Slide 49
      Two-monitor Configuration
4 focal powers separated by 0.6 diopters
workspace of 1.8 diopters; insertion of ophthalmic lenses allows adjustment
monitor & lens refresh of 180 Hz, so 45 Hz per eye per lens state
field of view of ~15 deg
Love, Hoffman, Hands, Gao, Kirby, & Banks (2009), Optics Express

## Slide 50: Complex materials
Pearl: Glossy
Rubber: Matte

## Slide 51
Kirschmann (1895)
Blake & Bülthoff (1990)
Muryy, Fleming, & Welchman (2013)
Reflection Geometry

## Slide 52
      Schematic of Lens
Do vergence-accommodation conflicts in stereo displays cause discomfort & fatigue?
If so, what can we do to minimize the discomfort & fatigue?
Love, Hoffman, Hands, Gao, Kirby, & Banks (2009)

## Slide 53: Optimization: in words (for Marty's benefit)
The input is a set of target images focused at different depths. The unknowns are the images to display on the presentation planes such that the result matches these target images.
Consider one of the target images, focused at a known depth. When the viewer focuses on that depth in the volumetric display, the image on each presentation plane is blurred by a known PSF. The resulting image seen by the viewer is the sum of these blurred images. We want this image to be the same as the target image.
We can compute a measure of error between the target image and the viewed image. We seek to minimize the total squared error across all target focus depths, as long as the presentation images remain within the displayable range.

## Slide 54: Optimized blending technique
The layers are calculated such that their sum approximates the original scene

## Slide 55: Example layers (linear blending)
mid-near
far
near
far-mid
Courtesy of Rahul Narain
Original scene
Layers

## Slide 56: Comparison of results
Linear Blending Technique
Optimization Technique

## Slide 57
Linear Depth-weighted Blending
near focus
p1
p2
p3
p4
far focus

## Slide 58
Reflection Geometry
Illumination sphere
object
virtual image

## Slide 59
Input: target images
with different focus depths
s1
sn
· · ·
?
?
?
?
Unknown: images to display
on presentation planes
p1
p2
p3
p4
Optimized Blending
Notes: The input is a set of target images focused at different depths. Unknowns are the images to display on the presentation planes such that the result matches these target images.
Consider one of the target images, focused at a known depth. When the viewer focuses on that depth in the volumetric display, the image on each presentation plane is blurred by a known PSF. The resulting image seen by the viewer is the sum of these blurred images. We want this image to be the same as the target image.
We compute a measure of error between the target image and the viewed image. We minimize the total squared error across all target focus depths, as long as the presentation images remain within the displayable range.

## Slide 60
Experimental Stimulus: Motion Parallax
reflection
Notes: Is this pinhole rendering?

## Slide 61
Experimental Stimulus: Motion Parallax
paint
Notes: Is this pinhole rendering?

## Slide 62
Bidirectional Reflectance Distribution Function
I: incoming light
R: outgoing light
δ angle between normal and half angle between θi and θr
ρd diffuse reflectance
ρs specular reflectance
α standard deviation (RMS) of surface slope
Ward (1992)
Notes: Check animations
Fix Hartung & Kersten
Check Wilcoxon title
Fix protocol slide

## Slide 63
Optimized Blending
near focus
p1
p2
p3
p4
far focus